## Slide 1: NAVIGATION TERMS
Indicated Airspeed is the airplane’s speed as indicated by the airspeed indicator.
True Airspeed is the actual speed of the airplane through the air mass.
Groundspeed is the speed of the airplane relative to the ground
Level Four 417.03a
OHP # 1

## Slide 2: NAVIGATION TERMS
Magnetic Meridian is the direction in which a compass needle will lie when influenced only by the Earth’s magnetic field.
Compass North is the direction in which a particular compass needle will lie when influenced by both the Earth’s magnetic field and local magnetic influences (deviation) in the airplane.
Level Four 417.03a
OHP # 2

## Slide 3: NAVIGATION TERMS
Azimuth, or bearing, refers to the direction to or from any point, measured as an angle clockwise from a meridian.
Wind is air in motion, especially a mass of air having a common direction or motion.
Drift, or drift angle, is the angle between the heading being flown and the track made good over the ground.
Level Four 417.03a
OHP # 3

## Slide 4: NAVIGATION TERMS
The Heading of an airplane is the angle between the longitudinal axis of the airplane at any moment and a meridian.
In other words, it is the direction the nose of the aircraft is pointing.
This is different than a bearing. A bearing from an aircraft to a particular location would not necessarily be the same as the direction the plane was heading.
Level Four 417.03a
OHP # 4

## Slide 5: NAVIGATION TERMS
Track (intended) is the direction an airplane intends to travel over the ground.
Track Made Good is the actual path traveled by the airplane over the ground.
Track Error is the angle between the required track and the track made good, measured in degrees either left or right of the required track.
Level Four 417.03a
OHP # 5

## Slide 6: NAVIGATION TERMS
Opening Angle is the angle between the required track and the track made good.
Closing Angle is the angle between the old required track and the new required track necessary to arrive at the destination.
Level Four 417.03a
OHP # 6